## Slide 1
BLUETOOTH VULNERABILITY RESEARCH: CRACKLE EXPLOIT LOCKHEED MARTIN
Team Evil Smurfs: Josh Minick, Vi Nguyen, Kaitlyn Malone, Kelly-Ann Downer, Jack Raymond
12/16/21

## Slide 2: Objective and Introduction
Obtain the LTK or Long Term Key from the pairing process between a target user and a target Bluetooth device
Bluetooth Sniffing is observing the traffic during a pairing process to obtain information
  With the sniffer we used, we needed multiple packets in order to decrypt using crackle
Crackle
    The required packets for Crackle to successfully decrypt are:
      Connection Request, pairing request and response, two random values (Mrand and Srand), two confirms (pairing confirm from each device), an encryption request and response, and a start encryption request.
    If you do not obtain all of these packets during the pairing process,
    the only troubleshooting tips were to repeat the process to sniff
    all of the required packets
12/16/21

## Slide 3: Challenges Faced
1. Downloading the dependencies in the proper locations
  This wasn't too much of an issue as it was fairly easy to fix, however the guides and examples online varied with what dependencies were required as well as download location for the crackle program itself.
2. Knowing which key type was being used for each device we tested
  Companies don't usually freely publish which pairing key type is used for their Bluetooth devices. There are a few pairing types such as Just Works, Passkey, and Out-Of-Band.
  To get around this issue we just tried each device multiple times using the different pairing key settings within Wireshark to see which delivered the most information.
3. Using the wrong Bluetooth sniffer
  Crackle apparently did not work with a Nordic brand Bluetooth sniffer during its earlier version. This was not mentioned except for in the closed issue comments in the GitHub.
  This was fixed in the later version of Crackle, so we downloaded
  the proper version that supported Nordic sniffers.
12/16/21

## Slide 4: Key Steps For Exploitation
Steps:
Scan for the Bluetooth device sending advertising packets
Collect the Bluetooth Low Energy packets through Wireshark
Decrypt the packets using Crackle
Prerequisite: Ensure the victim is attempting to pair a Bluetooth device
12/16/21

## Slide 5: Mitigation
12/16/21
Only pair Bluetooth devices when you are alone.
  By pairing when you know there are no bad actors around, they can't know that you're going to pair a device unless they see the process about to happen.
Keep devices out of pairing mode until you're ready to pair.
  When a device is in pairing mode it is sending advertising packets to devices within range which bad actors can use to gain information.

## Slide 6: References
https://github.com/mikeryan/crackle/blob/master/FAQ.md
http://lacklustre.net/projects/crackle/
https://infocenter.nordicsemi.com/index.jsp?topic=%2Fug_sniffer_ble%2FUG%2Fsniffer_ble%2Fintro.html
https://cdn-learn.adafruit.com/downloads/pdf/introducing-the-adafruit-bluefruit-le-sniffer.pdf
https://github.com/mikeryan/crackle/pull/36/commits/f9c1fe7c5185735aa6accdc53213db3b33f6ce3d
12/16/21